## Slide 1: 2.Hardware Description Languages
Computer Architecture

## Slide 2: Executive Summary
Motivation: Hardware functionality and complexity in the processor design is increasing over the years.
Problem: Computer Architect needs to reduce the project complexity to implement diverse hardware
Overview:
- Installation of Hardware Description Language (HDL) tools in the designer environment.
- Motivate the usage of Verilog HDL for designing at a higher level of abstraction.
- Design and testing based on modules for efficient reuse.
Conclusion: Using Verilog HDL the computer architect can reduce the design effort of designing complex hardware.

## Slide 3: Outline
Introduction
Working Environment
Verilog Syntax
Design Examples
Conclusions

## Slide 4: Introduction
Building blocks allows to implement large and complex systems.
  A building block can be defined on each abstraction level
    User programs: classes, functions, etc.
    Hardware: modules, gates, transistors, etc.
  Allows to focus on the function of the building block, instead of the lower-level details (e.g.: transistors timing).
Complex design needs to be verified and tested.
  First the design is simulated.
  Then, the design is synthetized (translated and ported) to a Field Programmable Gate Array (FPGA) for prototyping.
In our course we design a microprocessor, create a prototype using Verilog and an FPGA.

## Slide 5: Types of devices
 | Microprocessors | FPGAs | ASICs
 | Processor | FPGA | ASIC
Characteristics | General purpose hardware | Reconfigurable hardware | Custom design
Purpose | General | Prototyping | Max performance
Programming | Executable file | Bit file | Design masks
Program Development Time | minutes | days | months
Languages | C/C++,Python, etc. | Verilog/VHDL | Verilog/VHDL
Main Companies | Intel, ARM, AMD | AMD Xilinx, Intel Altera, Lattice | TSMC, UMC, ST, Global foundries
Examples | Intel i9 14900 | Xilinx Artyx 7 | NVIDIA H100, Google TPU v2

## Slide 6: Hardware Design
  Computer Architect needs a Hardware Description Language (HDL) to work at a higher level of abstraction.
  HDL allows to create complex designs, and provide both:
    Simulation
    - Inputs applied to circuit
    - Outputs checked for correctness
    - Millions of dollars saved by debugging in simulation instead of hardware
    Synthesis
    - Transforms HDL code into a netlist describing the hardware (i.e., a list of gates and the wires connecting them)

## Slide 7: Hardware Description Languages
HDLs specifies logic function or models the electronic design.
Additional computer-aided design (CAD) tool produces or synthesizes the optimized gates.
  Verilog
    developed in 1984 by Gateway Design Automation
    IEEE standard (1364) in 1995
    More popular in US than VHDL

## Slide 8: What is an FPGA?
https://www.youtube.com/watch?v=iHg0mmIg0UU

## Slide 9: General processor programming vs hardware description
Techniques used to exploit parallelism and concurrency because the program is restricted by the processor (CPU, GPU) characteristics.
Result after compilation: binary
Hardware is inherently parallel and concurrent (signals).
Compilation (almost) equivalent to synthesis
Result after synthesis: netlist
Netlist used to map and represent connectivity between gates.
Netlist can be used to create a chip.
Idea/requirement
Idea/requirement
Implement and testing C++/C, go, etc.
Implement and simulate VHDL, Verilog, etc.
Final program or app
Final chip (additional testing)

## Slide 10: Basys 3
This is an FPGA board
  The FPGA is on-board
    AMD/Xilinx Artyx 7

## Slide 11: Outline
Introduction
Working environment
Verilog Syntax
Design Examples
Conclusions

## Slide 12: Xilinx Vivado Suite
We use Vivado in Utec Labs
Lab computers have Vivado already installed.
    Vivado Standard (40GB, less than a pc game) in your laptop/desktop. – This is OPTIONAL
You can use EDAplayground for quick testing: https://edaplayground.com

## Slide 13: Outline
Introduction
Working environment
Verilog Syntax
Design Examples
Conclusions

## Slide 14: Basic Syntax
Verilog is case sensitive
  SomeName and somename are not the same!
Names cannot start with numbers:
  2good is not a valid name
Whitespaces are ignored
// Single line comments start with a //
/* Multiline comments
are defined like this */

## Slide 15: Precedence of Operations in Verilog
Highest
Lowest
~ | NOT
*, /, % | mult, div, mod
+, - | add,sub
<<, >> | shift
<<<, >>> | arithmetic shift
<, <=, >, >= | comparison
==, != | equal, not equal
&, ~& | AND, NAND
^, ~^ | XOR, XNOR
¦, ~¦ | OR, NOR
?: | ternary operator

## Slide 16: Number Representation in Verilog
Format: N’Bxx: 8’b0000_0001
  (N) Number of bits (default is 32 bits):
        - Expresses how many bits will be used to store the value
  (B) Base : Can be b (binary), h (hexadecimal), d (decimal), o (octal)
  (xx) Number: The value expressed in base
  Can also have X (invalid) and Z (floating), as values
  Underscore _ can be used to improve readability
Verilog | Stored Number | Verilog | Stored Number
4’b1001 | 1001 | 4’d5 | 0101
8’b1001 | 0000 1001 | 12’hFA3 | 1111 1010 0011
8’b0000_1001 | 0000 1001 | 8’o12 | 00 001 010
8’bxX0X1zZ1 | XX0X 1ZZ1 | 4’h7 | 0111
‘b01 | 0000 .. 0001 | 12’h0 | 0000 0000 0000

## Slide 17: Define a Module in Verilog
module example (a, b, c, y);
input a;
input b;
input c;
output y;
// here comes the circuit description
endmodule
Port list
(inputs and outputs)
ports have a declared type
a module definition
name of module
example

## Slide 18: Code Style
Codes are functionally equivalent:
module test ( a, b, y );
input a;
input b;
output y;
endmodule
module test ( input a,
input b, output y );
endmodule
port name and direction declaration can be combined
We recommend using this

## Slide 19: Defining Multi-bit Input and Output
You can also define multi-bit Input/Output (Bus)
  [range_end : range_start]
  Number of bits: range_end – range_start + 1
Example:
a represents a 32-bit value, so we prefer to define it as: [31:0] a
It is preferred over [0:31] a which resembles array definition
It is good practice to be consistent with the representation of multi-bit signals, i.e., always [31:0] or always [0:31]
input [31:0] a; // a[31], a[30] .. a[0]
output [15:8] b1; // b1[15], b1[14] .. b1[8]
output [7:0] b2; // b2[7], b2[6] .. b2[0]
input c; // single signal

## Slide 20: Manipulating Bits
Verilog allows to manipulate bits in different ways:
// Bit Slicing: assign partial buses
wire [15:0] longbus;
wire [7:0] shortbus;
assign shortbus = longbus[12:5];
// Concatenation: Concatenating is by {}
assign y = {a[2],a[1],a[0],a[0]};
// Duplication: Possible to define multiple copies
assign x = {a[0], a[0], a[0], a[0]}
assign y = { 4{a[0]} }

## Slide 21: Two Main Styles of HDL Implementation
Structural
  Each module contains other modules (instances)
  Describes a hierarchy
  Can contain gate-level description
Behavioral
  Module body contains functional description of the circuit
  Contains logical and mathematical operators
  Level of abstraction is higher than gate-level
    Many possible gate-level realizations of a behavioral description
Real implementations can use a combination of both
Notes: TODO: stick to those rather than dataflow, switch level

## Slide 22: Structural HDL: Instantiating a Module
i_first
i_second
Module “top” is built from two instances of module “small”

## Slide 23: Structural HDL Example
Module Definitions in Verilog
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 24: Structural HDL Example
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Defining wires (module interconnections)
i_first
i_second

## Slide 25: Structural HDL Example
The first instantiation of the “small” module
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// instantiate small once
small i_first ( .A(A),
.B(SEL),
.Y(n1) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 26: Structural HDL Example
The second instantiation of the “small” module
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// instantiate small once
small i_first ( .A(A),
.B(SEL),
.Y(n1) );
// instantiate small second time
small i_second ( .A(n1),
.B(C),
.Y(Y) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 27: Structural HDL Example
Short form is not good practice as it reduces code maintainability
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// alternative
small i_first ( A, SEL, n1 );
/* Shorter instantiation,
pin order very important */
// any pin order, safer choice
small i_second ( .B(C),
.Y(Y),
.A(n1) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
i_first
i_second

## Slide 28: Behavioral HDL: Defining Functionality
module example (a, b, c, y);
input a;
input b;
input c;
output y;
// here comes the circuit description
assign y = ~a & ~b & ~c |
a & ~b & ~c |
a & ~b & c;
endmodule
AND
y
AND
AND
OR
a
b
c

## Slide 29: Outline
Introduction
Working environment
Verilog Syntax
Design Examples
Conclusions

## Slide 30: Exercise
Draw the logic diagram of the circuit using logic gates.
Write a Verilog description of the circuit.
Write a testbench to simulate all input combinations and verify correctness.

## Slide 31: Verilog
// Boolean function:
// Y = ((A & B) | (~C & D)) & (A | ~B | C)
module logic_circuit ( A, B, C, D, Y);
input A, B,C, D;
output Y;
assign Y = ((A & B) | (~C & D)) & (A | ~B | C);
endmodule

## Slide 32: Testbench v1
`timescale 1ns/1ps
module tb_logic_circuit;
reg A, B, C, D; //only on testbench for ‘writing’ values
wire Y;
// Instantiate the circuit under test
logic_circuit uut (
.A(A), .B(B), .C(C), .D(D), .Y(Y) //connect each one
);
initial begin
$display("Time | A B C D | Y");
$display("--------------------");
// Test case 1
A = 0; B = 0; C = 0; D = 0;
#10 $display("%4t | %b %b %b %b | %b", $time, A, B, C, D, Y); //this represents time passing
// Test case 2
A = 0; B = 1; C = 0; D = 1;
#10 $display("%4t | %b %b %b %b | %b", $time, A, B, C, D, Y);
// Test case 3
A = 1; B = 0; C = 1; D = 0;
#10 $display("%4t | %b %b %b %b | %b", $time, A, B, C, D, Y);
// Test case 4
A = 1; B = 1; C = 0; D = 1;
#10 $display("%4t | %b %b %b %b | %b", $time, A, B, C, D, Y);
// Test case 5
A = 1; B = 1; C = 1; D = 1;
#10 $display("%4t | %b %b %b %b | %b", $time, A, B, C, D, Y);
$finish;
end
endmodule
test
dut
(design under test)
testbench

## Slide 33: Testbench v2
`timescale 1ns/1ps
module tb_logic_circuit;
reg A, B, C, D;
wire Y;
// Instantiate the circuit under test (UUT)
logic_circuit uut (
.A(A), .B(B), .C(C), .D(D), .Y(Y)
);
initial begin
$display("A B C D | Y");
$display("----------------");
// Iterate over all 16 input combinations
for (integer i = 0; i < 16; i = i + 1) begin //be careful using for
{A, B, C, D} = i;
#10; //this represents time passing
$display("%b %b %b %b | %b", A, B, C, D, Y);
end
$finish;
end
endmodule
Loops are common in testbenches, not so much in hardware modules. Be careful.

## Slide 34: Outline
CS3501-COMPUTER ARCHITECTURE
Introduction
Working environment
Verilog Syntax
Design Examples
Conclusions

## Slide 35: Summary
  Hardware Description Languages (HDLs) abstracts the digital design to a model.
    Simulation as a tool for verification, programming as a tool for creation.
  We introduced the Verilog syntax.
    Verilog is an HDL, used for hardware description not for user program implementation.
    Logic gates (with transistors) as a starting point.
  We can evaluate our designs using a high-level language.
    Testbenches are used as a testcase evaluation of the hardware block.
    Testbenches are not part of the module. Remember: only used for testing.
  We conclude that using the logic gate arrays, we can create our own designs!

## Slide 36: 2.Hardware Description Languages
Computer Architecture